UniClOGS Power Delivery Board
Documentation for board rev 2 by Benjamin Crall
# Power Outputs:
Output channels can be configured for one of several modes. Output configuration is done by populating or leaving some other components unpopulated. A + denotes a current leaving the board, and a - denotes a current entering the board. Note that all banks do not support all current modes. Do not populate components that are not specified. Ensure that the output current from all outputs on each power input does not exceed the maximum input current.
## Bank A:
### Available modes:
- -500mA
- +16A
- +16A with soft start
### Configuration Instructions:
The channel supports 12-24AWG wire
Each channel may be configured independently
If you populate the P channel MOSFETs, populate the 10k pullup resistors
Use the 3pad jumper to select 5 or 12v for the +16A mode
In soft start mode, adjust Rgate to adjust soft start time
Mode	Dual MOSFET	P MOSFET	Rgate	C	2pad Jumper
-500mA	Yes				Jumped
+16A	Yes	Yes	1k		Open
16A soft-start	Yes	Yes	680k	Yes	Open

## Bank B and C:
### Available Modes:
- ±1.5A
- -500mA
### Configuration Instructions:
These channels support 16-26AWG wire
A channel pair is an even channel and the next odd channel (e.g. 0 and 1)
Each channel pair must be configured for the same mode.
Mode	Dual Driver	Dual MOSFET
-500mA		Yes
±1.5A	Yes

# Power Inputs
## Input:
Power is supplied to the 3 position connector on the left edge of the board. The pinout is
+12V 25A
GND 16A
+5V 16A

The board does not draw or provide any power to the raspberry pi
Each input supports 8-24AWG wire.
## Protection:
Each power input has reverse polarity protection.
There is no overcurrent protection. Be sure to not to draw too much current from single or combination of outputs. See the channel documentation above to see the individual channel output currents.
- Channel A supports up to 18A of total output current on 5V
- Channel A and B share 18A of total output current on 12V
- Channel C has 7A of total output current at 12V independent of channels A and B
## Outputs:
Power indicator LEDs are in the lower left corner of the board. Next to them are power output pins. These pins are capable of 1A each, except for 3.3V which is capable of 250mA
# Analog Inputs
## Main Inputs
Each board has 4 analog inputs available on the top left 8 pin connector. The pinout is
ADC0	Agnd	ADC1	Agnd	ADC2	Agnd	ADC3	Agnd

Agnd is connected to general ground by the left link at the top of the Analog In section. This link can be replaced by a 0805 ferrite bead if desired.
Be careful to avoid ground loops when connecting to the Agnd pins
## .1” Inputs
The analog inputs are also available on the .1” header above the main connector. The pinout of this connector is
ADC0	ADC1	ADC2	ADC3	Agnd

# Data Connectors
## 1x IDC 40 pin connector for the Raspberry pi
	01	02
SDA1	03	04
SCL1	05	06	GND
TX3	07	08	TX0
GND	09	10	TX0
TMP_ALERT (GPIO17)	11	12
ADC_RDY (GPIO27)	13	14	GND
	15	16
	17	18
	19	20	GND
RX4	21	22
	23	24	TX2
GND	25	26
TX2	27	28	RX2
RX3	29	30	GND
IO_RESET (GPIO6)	31	32	TX5
RX5	33	34	GND
	35	36
	37	38
GND	39	40

The 3.3V and 5V pins on the Raspberry Pi are not connected
## 4 pin I2C1
GND	3.3V	SCL1	SDA1

This is the internal I2C bus used to communicate with the card
## 4 pin (2x2) Signals
ADC_RDY	TMP_ALERT
IO_RESET	gnd

## 3 pin Serial
gnd	RX (in)	TX (out)

These headers connect to (from top to bottom) UART0, UART2, UART3, UART4, UART5
UART2 can also double as I2C0. To use this as I2C0, populate R4 and R5, otherwise leave them empty
gnd	SCL0	SDA0

# Signal Configuration
All I2C devices on the board are connected to I2C1 on the Raspberry Pi.
## Power Output Banks
The power output banks are controlled by MAX7310 I2C expanders. Each power output bank can be configured to 1 of 8 I2C addresses. The I2C address for each bank is between 0x20 and 0x27. The 3 jumpers configure the 3 lower bits of the address, and the binary address is 0100{AD2}{AD1}{AD0}. The default jumpers connect the address pins to SCL (0) and SDA (1). See the datasheet if more addresses are required. Banks A,B and C have the default addresses of 0x20, 0x21, and 0x22. The active low IO_RESET signal is connected to the Raspberry Pi. Ensure that this signal is held high through boot to not reset the expanders. IO_RESET is pulled high by a 4.7k resistor. See the datasheet for device usage.
## ADC
The ADC is an ADS1115IDGS I2C ADC with a default address of 0x48. Use the jumper to select the alternate address of 0x49 if required. The active low ADC_RDY signal is connected to the Raspberry Pi connector. ADC_RDY is pulled high by a 4.7k resistor. See the datasheet for device usage.
## Temperature Sensor
The temperature sensor is an ADT7410TRZ I2C Temperature Sensor. The default address is 0x4A. Use the left jumper to select the alternate address of 0x4B if required. Note that only the A0 pin is used and the A1 pin is tied to 3.3V to avoid address conflicts with the ADC. Additionally, the sensor can also create two alert or alarm signals which are active low and connected to TMP_ALERT. Use the right jumper to select between the “Critical Overtemperature” (CT) and “Overtemperature and Undertemperature” (INT) signals. TMP_ALERT is pulled high by a 4.7k resistor. See the datasheet for device usage.
# Using Multiple Boards
Two of these boards may be used in together to provide additional output channels. To do this, the first board should be configured in the default configuration. On the second board:
- Change the AD2 jumper on each bank from 0 to 1. Banks A, B, and C will now be on I2C addresses 0x24, 0x25, and 0x26
- Change the address jumper on the ADC to 0x49
- Change the address jumpers on the temperature sensor to 0x4B
- Connect the 40 pin IDC connector to both boards in parallel
  - Alternately, connect the 4 pin (2x2) Signals connector and the 4 pin (2x2) Signals connector except for the 3.3V pin directly between the two boards